## Slide 1
Wireless Power Transfer
1
C1C Henry
C1C Hermanson
C1C Pak
C1C Singh

## Slide 2: Overview
Technical Discussion/Attack Vector Review - NSTR
Motivation - NSTR
Problem Statement - NSTR
Key Sprint Accomplishments
Results
Challenges
Sprint 7
Future Work - NSTR
Questions

## Slide 3: Technical Discussion
WPT is wireless point to point transmission protocol of electrical energy
Many implementations but Qi is the industry standard
  Alternatives: AirFuel, Proprietary Near Field Magnetic Coupling, RF, Ultrasound
Delivers a variable amount of voltage to device depending on power requirements
New technology that lacks security capabilities and has vulnerabilities
  Malicious messages can be sent between transmitter and receiver to alter power transmission
  Messages between transmitter and receiver can be observed to gain information about receiver

## Slide 4: Motivation
Wireless Power Transfer has become an industry standard being incorporated into more and more areas of technology
  Personal Electronics, Healthcare Devices, Electric Vehicles
Exploit techniques and results found in this experiment can potentially be generalized
This research will create a foundation for further experimentation and TTP development
  Findings expanded to other wireless non-networked point-to-point connections

## Slide 5: Qi Specs
AC frequency in the primary coil
  110 and 205 kHz for the “low power” Qi chargers (up to 5 W)
  80 and 300 kHz (up to 120 W) for the “medium power” chargers
Optimized to operate from a 5V USB power supply
  Uses “smart power limiting” to adjust the output power automatically to compensate for power-limited supplies

## Slide 6: Motivation
Wireless Power Transfer has become an industry standard being incorporated into more and more areas of technology
  Personal Electronics, Healthcare Devices, Electric Vehicles
Exploit techniques and results found in this experiment can potentially be generalized
This research will create a foundation for further experimentation and TTP development
  Findings expanded to other wireless non-networked point-to-point connections

## Slide 7: Problem Statement
IDENTIFY
  Vulnerabilities
  How to exploit
  How to defend
APPLY
  Proof of concept – hijacking
  Proof of concept – eavesdropping
  Interpretation of results
EXPAND
  Provide research to NRO
  Observe various side channel-attacks
  Create security mitigations – Software Based Encryption
  Expand to larger technologies

## Slide 8: Key Sprint Accomplishments
NRO Presentation
Signature Analysis
Signature Visualizations
.qid File Utilization
Qi Communication Research
Encryption Research

## Slide 9: NRO Presentation
Developed two slide decks for NRO presentation (40 slides and 10 slides)
Successfully briefed the NRO representatives about key accomplishments and research

## Slide 10: Fingerprinting
  GUI deemed impractical given time constraints
  Graphing capability added to analyze signatures

## Slide 11: Signature Analysis
Signatures reinforce research
Working on more applications
Still inputting data by hand

## Slide 12: .qid Update
Hex file appears to contain metadata for sniffer software
Known packets could not be found with ctrl + f

## Slide 13: Qi Communication
The Rx monitors the battery and the charging process and uses ASK Modulation.
The Rx communicates at 2Kbs using a transistor array.
The Tx communicates at 200Bps using FSK modulation.

## Slide 14: Qi Sniffer
Qi Development System
  Communications insight
  Seeking further interpretation of qid filetype

## Slide 15: Linear Feedback Shift Register (LFSR) Encryption
LFSR is a stream cipher
  Easily integrated into small devices
Basic level of encryption
Little to no effect on speed

## Slide 16: Existing Challenges
ECE Injection Crafting
Qi Simulation layered with Encryption
.qid file parsing
Better tools than waveform generator for injection
Hardware knowledge

## Slide 17: Discussion of Progress and Implications
Based on research and testing findings, Qi is an unsecure standard
  It is susceptible to multiple attack vectors (based on proof of concept)
  It is open air and thus susceptible to snooping (based on proof of concept)
There are some available methods to attempt to alleviate these vulnerabilities
  Encryption (working towards proof of concept)
Other technologies/standards could be susceptible in the same ways
  AirFuel, Proprietary Near Field Magnetic Coupling, RF, Ultrasound, EV Charging, Medical devices

## Slide 18: Sprint 7 – Taskers/COA
Soft Encryption Development
  Simulation representation expansion
  Encryption timing validation and testing
    LSFR, expand to further encryption schemes
  (Packet Snooping and Injection mitigation)
Proceed with Fingerprinting
  Expand visuals
  Specific Emitter Identification
Constant Charge Transition (Charge/Don't Charge)
  Waveform Generator Interface
  Progress in OS DoS

## Slide 19: Future Work
Modification of Qi packets
  Qi communication packets are interpreted on the receiver device, modification of the data component within the Negotiation Phase may allow code execution or data exfiltration on the receiver device
Development and testing of Qi Protection Mechanisms
  Hardware or Software based cryptography
  Injection/packet modification detection
Applications with laser-based point-to-point communication
  Non-networked systems

## Slide 20: Questions?