## Slide 1
Wireless Power Transfer
1
C1C Pak
C1C Singh
C1C Henry
C1C Hermanson

## Slide 2: Overview
Executive Summary
Technical Discussion
Motivation
Problem Statement
Related Work
Methodology
Results
Discussion
Future Work
Questions

## Slide 3: Executive Summary
Review fundamentals of WPT and associated vulnerabilities.
Discussion of action items researched and completed throughout this Semester.
Review significant developments and existing challenges related to the research.
Consider the next phase of research and look ahead at long-term goals of this Capstone Project.
Consider the long-term implications of this capstone project.

## Slide 4: Technical Discussion
WPT is wireless point to point transmission of electrical energy
Many implementations but Qi is the industry standard
  Alternatives: AirFuel, Proprietary Near Field Magnetic Coupling, RF, Ultrasound
Delivers a variable amount of voltage to device depending on power requirements (5-15 Watts)
New technology that lacks security capabilities and has vulnerabilities
  Malicious messages can be sent between transmitter and receiver to alter power transmission
  Messages between transmitter and receiver can be observed to gain information about receiver

## Slide 5: WPT Attack Vectors
Hijacking
  Injection of adversarial magnetic signals on the power transmitter to hijack the communication channel
  Disruption of magnetic field (via well crafted injection) between transmitter and receiver – cause inefficient power transfer
  Control of power transfer process
Eavesdropping
  Qi has lack of encryption and authentication mechanisms
  Snoop communication between transmitter and receiver
  Infer activity of receiver device
  Q ID & C allows basic device identification

## Slide 6: Sprint Organization
Utilized Jira Software to track the sprint process

## Slide 7: Research Timeline
Sprint 1
  Conducting research about WPT and related technologies
  Acquired necessary materials to replicate experiments
Sprint 2
  Generated code to achieve demodulation
  Completed hijacking proof of concept
Sprint 3
  Researched Qi packet signatures
  Gained voltage signatures
  Researched WPT interaction with operating system
Sprint 4
  Researched and simulated software encryption
  Explored alternative defensive mitigations

## Slide 8: Motivation
Wireless Power Transfer has become an industry standard being incorporated into more and more areas of technology
  Personal Electronics, Healthcare Devices, Electric Vehicles
Exploit techniques and results found in this experiment can potentially be generalized
This research will create a foundation for further experimentation and TTP development
  Findings expanded to other wireless non-networked point-to-point connections

## Slide 9: Problem Statement
IDENTIFY
  Vulnerabilities
  How to exploit
  How to defend
APPLY
  Proof of concept – hijacking
  Proof of concept – eavesdropping
  Interpretation of results
EXPAND
  Provide research to NRO
  Observe various side channel-attacks
  Create security mitigations – Software Based Encryption
  Expand to larger technologies

## Slide 10: Key Accomplishments to Date
Replicated Experiment
  Wireless Charging Power Side-Channel Attacks
Demonstrated Injection
Demonstrated Snooping
Developed Demodulation Program
Researched various aspects of WPT and related attacks/mitigation
  Encryption
  Signature Analysis
  OS Interactions

## Slide 11: Summary of Related Work
CoDoC: A Novel Attack for Wireless Rechargeable Sensor Networks through Denial of Charge
  WPT networks susceptible to Denial of Charge (DoC) attacks
  Can disrupt network reliability, network functionality, and possibly trigger event loss
Safe and Secure Wireless Power Transfer Networks: Challenges and Opportunities in RF-Based Systems
  Handful of attacks – safety, charging, interference, spoofing, software, and monitoring attacks
  Countermeasures should be implemented as small and energy-efficient protocols to ensure safe and secure energy transfer
Wireless Charging Power Side-Channel Attacks
  the amount of current being drawn from the charger can be used to determine which applications are being used by the mobile device
  Shows weaknesses of such attacks; ex: the longer a device is being used, the less accurate the estimate is

## Slide 12: Day 1 Methodology
Taking inventory of all equipment
  created a list of needed equipment using the Security of Qi Standards research paper and experiment as a guide
Soldered leads onto the stripped coils from the wireless chargers
  begin taking initial reads of the Qi communications
Focused on analyzing the readouts from the oscilloscope to attempt to demodulate the bits and determine the communication process of Qi standard adhering equipment
Challenges in the form of demodulation - initially unable to extrapolate exact bits from the oscilloscope

## Slide 13: Demodulation - Methods
MatLab
  Strategy: Read waveform data into MatLab and use premade code for demodulation filters
  Problems: Familiarity with tool, getting data into Simulink
Oscilliscope Filters / TekScope
  Strategy: Use filters directly on oscilloscope /within TekScope suite
  Problems: No license for bus features, no bus for Qi demodulation
Python
  Strategy: Read captured waveform data from stored file to apply demodulation filters
  Problems: One packet at a time – limited capture size

## Slide 14: MatLab Demodulation
MATLAB object driver to read waveform/import data
Simulink to apply lowpass filter

## Slide 15: TekScope Demodulation
TekScope software use:
  Manchester Bus
  Low pass filter
  A lot of other attempts
    Filters
    Busses
    Math

## Slide 16: Python Demodulation

## Slide 17: Packet Interception
Captured Signal
Captured Signal Demodulated
Signal Strength Status Update 1

## Slide 18: Packet Injection
Crafted Waveform Signal
  Frequency: 80kHz
  Amplitude: 10Vpp
  Offset: 0V
  Phase: 0V
Channel Overload
              (Magnetic Signal Interference)
Injection Test 1
1 1 1 1 1 1 1 1 1 1 1 1 0 1 1 1 0 1 0 1 0 1 1 1 0 1 0 1 0 1 0 1 1 1 0 1 1 1 0 1 0 1 0 1 1

## Slide 19: Signature Analysis
Voltage readings taken at three different battery percentage values (100%, 50%, 0%)
.csv files loaded into python plotting program
Voltage differences noticed in 100% battery charging
Individual samples (not averages)

## Slide 20: Android OS
Android Open Source Project
  Mirror of existing build – contains previous builds
Android Code Search
  Tool – allow developers to view Android source code

## Slide 21: Android OS
Viewed and analyzed OS source code
Searching for how the Android operating system interacts and interprets, if at all, any incoming Qi communications.
No prior publications found – researched from ground up
Cumulative Time Spent: ~32 Hours

## Slide 22: Android OS
Findings:
  No evidence to suggest that the OS controls the process overtly (besides normal battery function and recognizing that the phone is receiving power).
  We do believe that our findings give us enough of a confirmation to conclude that this vector is not a real possibility for this group to pursue.
  OS is unlikely to be anything more than severely limited.
  Best vector for attack using this technology will remain as voltage analysis (side channel attacks using voltage) and as denial-of-service style attacks using injection methods.

## Slide 23: Charging Simulation

## Slide 24: Charging Simulation

## Slide 25: Eavesdropping Defense - Noise
Noise makes power signature less readable
Signature accuracy drops from 91.2% to 44.4%
Can be achieved with waveform generator and adversarial coil

## Slide 26: Eavesdropping Defense - Encryption
Using Bluetooth as a model
  Bluetooth implements the following systems:

## Slide 27: Software Based Encryption

## Slide 28: Results Summary + Discussion
Produced Packet Interception and Decoding for Snooping Purposes
Produced Packet Injection with Adversary Binary
Android OS
  No further research suggested, rule out IOS
Software Based – Authentication
  Basic key exchange created by transmitting node
Software Based – Encryption
  Chaotically regulated encrypted switching frequency
Signature Analysis
  Identified discernable variances in data gathered at different thresholds
  Need to work on quantifiable differences

## Slide 29: Spring Semester
Packet Sniffer Acquired
  Expand Snooping Research
  Differentiate applications – based on power usage
  Extract data from communications
    In depth packet analysis (identifiers, etc)
  Extract user input from receiver
Customized Injection Development
  Craft Hardware
  Develop Signal
  Experiment with timing
Soft Encryption Development

## Slide 30: Future Work
Modification of Qi packets
  Qi communication packets are interpreted on the receiver device, modification of the data component within the Negotiation Phase may allow code execution or data exfiltration on the receiver device
Applications with laser-based point-to-point communication
  Non-networked systems
Development of Qi Protection Mechanisms
  Hardware or Software based cryptography
  Injection/packet modification detection

## Slide 31: Questions
31