## Slide 1
Wireless Power Transfer
1
C1C Henry
C1C Hermanson
C1C Pak
C1C Singh

## Slide 2: Executive Summary
Review fundamentals of WPT and associated vulnerabilities
Action items researched and completed
Significant developments and existing challenges
Next phase of research
Long-term implications and goals of research

## Slide 3: Technical Discussion
WPT is wireless point to point transmission protocol of electrical energy
Many implementations but Qi is the industry standard
  Alternatives: AirFuel, Proprietary Near Field Magnetic Coupling, RF, Ultrasound
Delivers a variable amount of voltage to device depending on power requirements
New technology that lacks security capabilities and has vulnerabilities
  Malicious messages can be sent between transmitter and receiver to alter power transmission
  Messages between transmitter and receiver can be observed to gain information about receiver

## Slide 4: Qi Specs
AC frequency in the primary coil
  110 and 205 kHz for the “low power” Qi chargers (up to 5 W)
  80 and 300 kHz (up to 120 W) for the “medium power” chargers
Optimized to operate from a 5V USB power supply
  Uses “smart power limiting” to adjust the output power automatically to compensate for power-limited supplies

## Slide 5: Qi – Protocol Overview
Ping Phase
  The Power Transmitter tries to establish communications with a Power Receiver.
Configuration Phase
  Power Receiver sends basic identification and configuration data to the Power Transmitter. Both sides use this information to create a baseline Power Transfer Contract. (Decide to use Baseline or Extended Protocol)
Negotiation Phase
  The Power Transmitter and Power Receiver establish an extended Power Transfer Contract containing additional settings and limits. (Not present in baseline protocol)
  Power Receiver provides design information to the Power Transmitter
Power Transfer Phase
  Power transfer to the Power Receiver’s Load. In the Extended Protocol, the Power Transmitter and Power Receiver perform a system calibration at the start of this phase.
  Interruptions may occur – renegotiate an element of the Power Transfer Contract. (power transfer remains uninterrupted)

## Slide 6: WPT Attack Vectors – Overview (1)
Hijacking
  Injection of adversarial magnetic signals on the power transmitter to hijack the communication channel
  Disruption of magnetic field (via well-crafted injection) between transmitter and receiver – cause inefficient power transfer
  Control of power transfer process

## Slide 7: WPT Attack Vectors – Overview (2)
Eavesdropping
  Qi has lack of encryption and authentication mechanisms
  Snoop communication between transmitter and receiver
  Infer activity of receiver device
  Qi Sniffer allows basic device identification

## Slide 8: Motivation
Wireless Power Transfer has become an industry standard being incorporated into more and more areas of technology
  Personal Electronics, Healthcare Devices, Electric Vehicles
Exploit techniques and results found in this experiment can potentially be generalized
This research will create a foundation for further experimentation and TTP development
  Findings expanded to other wireless non-networked point-to-point connections

## Slide 9: Problem Statement
IDENTIFY
  Vulnerabilities
  How to exploit
  How to defend
APPLY
  Proof of concept – hijacking
  Proof of concept – eavesdropping
  Interpretation of results
EXPAND
  Provide research to NRO
  Observe various side channel-attacks
  Create security mitigations – Software Based Encryption
  Expand to larger technologies

## Slide 10: Key Accomplishments to Date
Replicated Experiment
  Wireless Charging Power Side-Channel Attacks
Demonstrated Injection
Demonstrated Snooping
Developed Demodulation Program
Researched various aspects of WPT and related attacks/mitigation
  Signature Analysis
  OS Interactions
  Qi Sniffer
  Fingerprinting (Script)
  Encryption
Authored Research Paper

## Slide 11: Packet Interception
Captured Signal
Captured Signal Demodulated
Signal Strength Status Update 1

## Slide 12: Packet Injection
Crafted Waveform Signal
  Frequency: 80kHz
  Amplitude: 10Vpp
  Offset: 0V
  Phase: 0V
Capable of 0101 injection
Channel Overload
              (Magnetic Signal Interference)
Injection Test 1
1 1 1 1 1 1 1 1 1 1 1 1 0 1 1 1 0 1 0 1 0 1 1 1 0 1 0 1 0 1 0 1 1 1 0 1 1 1 0 1 0 1 0 1 1

## Slide 13: Scripted Packet Generation
Generates Qi Signal – Exported via output csv file
Converts binary data into modulated signal utilizing a user specified sampling rate and clock frequency
Two types of Packets
  End Power Transfer (EPT) Control 1
  Control Error (CE) Control 1
Stages
  Preamble (Between 11 and 25 bits)
  Header
  Data Message
  Checksum

## Slide 14: Injection Via Waveform Generator
Utilizes csv files to inject crafted signals
Capture interactions via qi sniffer
Demonstrated greater overlap with signal injection
Existing Challenge
  timing and overlapping of signal messages
  Outright injection vs message overlap

## Slide 15: Qi Communication
The Rx monitors the battery and the charging process and uses ASK Modulation.
The Rx communicates at 2Kbs using a transistor array.
The Tx communicates at 200Bps using FSK modulation.

## Slide 16: Qi Sniffer
Qi Development System
  Sniffer Events, Event Properties, Timing Window

## Slide 17: Fingerprinting
Qi sniffer provides important information for fingerprinting
  Manufacturer
  Unique Qi serial number
  Charge status
  Qi Version

## Slide 18: Software Based Encryption

## Slide 19: Linear Feedback Shift Register (LFSR) Encryption
LFSR is a stream cipher
  Easily integrated into small devices
Basic level of encryption
Little to no effect on speed
Simulink Program created by Lt. Col McGinthy

## Slide 20: Existing Challenges
ECE Injection Crafting
Overlap of injected and transmitted signal
Qi Simulation layered with Encryption
Collecting data from Qi Sniffer software and making it usable

## Slide 21: Discussion of Progress and Implications
Based on research and testing findings, Qi is an unsecure standard
  It is susceptible to multiple attack vectors (based on proof of concept)
  It is open air and thus susceptible to snooping (based on proof of concept)
There are some available methods to attempt to alleviate these vulnerabilities
  Encryption (based on proof of concept)
Other technologies/standards could be susceptible in the same ways
  AirFuel, Proprietary Near Field Magnetic Coupling, RF, Ultrasound, EV Charging, Medical devices

## Slide 22: Lessons Learned
Document, document, document
  Overcomplicating the process with software can be detrimental to efficiency
Asking for help from the experts (or the tech support) is ok
Planning for research and software development are different
Some avenues explored will not work

## Slide 23: Future Work
Work with ECE to brainstorm additional ways forward and new ways to approach
  Lt Col Rogers
Improved signal injection
  Injected signal is properly interpreted allowing for denial of charge or device overcharge
Development and testing of Qi Protection Mechanisms
  Hardware or Software based cryptography
  Injection/packet modification detection
Applications with laser-based point-to-point communication
  Non-networked systems

## Slide 24: Questions?